## Slide 1: Fluid physical properties

## Slide 2: Properties of Fluid
Density
- Density, ρ is the mass per unit volume.
Units: Kilograms per cubic metre, kg / m3
Dimensions: M/L3
Typical values:
Water = 1000 kg/m3 , Mercury = 13546 kg/m3

## Slide 3
Specific Weight
- Specific weight, γ is the weight per unit volume.
Units: Newton’s per cubic meter, N / m3
Dimensions: M/L2T 2 .
Typical values:
Water =9814 N/m3 , Mercury = 132943 N/m3

## Slide 4
Relative Density
- Relative density, σ is the ratio of the fluid density to the water density.
Units: None, since a ratio is a pure number.
Dimensions: 1.
Typical values: Water = 1, Mercury = 13.5

## Slide 5
Viscosity
- Viscosity, μ is the property of a fluid, due to cohesion
and interaction between molecules, which offers
resistance to sheer deformation.
Units N m-2 ; kg m-1s-2
Dimensions ML-1T -2
Typical values:
Water =1.14 x 10-3 kgm-1 s-1 ,
Air =1.78 x 10-5 kgm-1 s-1 ,
Mercury =1.552 kgm-1 s-1

## Slide 6
Dynamic Viscosity
- Dynamic viscosity, ν , is defined as the ratio of
viscosity to mass density.
Units: square meters per second, m2 s-1
Dimensions: L2T -1 .
Typical values:
Water =1.14 x 10-6 m2 s-1 , Air =1.46 x 10-5 m2 s-1 ,
Mercury =1.145 x 10-4 m2 s-1