## Slide 1: Pressure Measurement By Manometer
The Piezometer Tube Manometer
The simplest manometer is a tube, open at the top, which is attached to the top of a vessel containing
liquid at a pressure (higher than atmospheric) to be measured. An example can be seen in the figure
below. This simple device is known as a Piezometer tube. As the tube is open to the atmosphere the
pressure measured is relative to atmospheric so is gauge pressure.

## Slide 3
P A = ρ g h1
P B = ρ g h2
The ‘U’-Tube Manometer
Using a ‘U’-Tube enables the pressure of both liquids
and gases to be measured with the same instrument.
The ‘U’ is connected as in the figure below and filled
with a fluid called the manometric fluid. The fluid
whose pressure is being measured should have a mass
density less than that of the manometric fluid and the
two fluids should not be able to mix readily - that is,
they must be immiscible.

## Slide 5
Pressure in a continuous static fluid is the same at any horizontal level so,
pressure at B = pressure at C
P B = P C
But,
PB = PA + ρ g h
PC = ρman g h2
PA = ρman g h2 – ρ g h1

## Slide 6
Measurement Of Pressure Difference Using a ‘U’-Tube Manometer
If the ‘U’-tube manometer is connected to a pressurized vessel at two points the pressure difference between these two points can be measured.
PC = PD
PC = PA + ρ g ha
PD = PB + ρ g (hb – h) + ρman g h
PA – PB = ρ g (hb – ha) – (ρman – ρ) g h